TENDER SPECIFICATIONS

Main Unit (in metallic box), including:

Industrial Controller:

ABB Controller Cm30.

Display: Color 1/4 VGA TFT, liquid crystal display (LCD) with built-in backlight.

Language: English, German, French, Italian and Spanish.

Operator keypad: 6 tactile membrane keys.

Password protection: Basic/Advanced user-assigned password protection.

Trend display:

Recording of 2 variables.

Configurable sample rate (1 second to 5 minutes).

Control parameters:

Proportional band: 0 to 999.9 %.

Integral: 0 to 10000 s.

Derivative: 0 to 999.9 s.

Manual Reset 0.0 to 100 %.

Autotune: On-demand calculation of control settings.

Process alarms:

Number: 8.

Types: High/Low process and High / Low latch.

Acknowledgement: Via front panel keys or digital signals.

Source: Fully configurable (for example, PV, analog input, math block inbuilt, OP control loop deviation).

Hysteresis: Level and time.

Alarm enable: Enable/Disable of individual alarms via a digital signal.

Analog inputs:

Number: 2.

Complete configurable process input: voltage (V or mV), current (mA), resistance (ohms), Thermocouple, 3-Wire RTD, frequency, pulse, volt-free digital input and 24V digital input.

Selectable set points via software (remote from the computer) or front panel.

Analog/Digital output:

Number: 1.

Type: Configurable as analog or digital pulse.

Analog range: 0 to 20 mA (programmable).

Control output types (Configurable through software):

Current proportioning/Voltage proportioning (using resistor).

Time proportioning.

On/Off.

Motorized valve with feedback.

Motorized valve without feedback.

Split output with combinations of relay digital O/P and current O/Ps.

Relays:

Number: 2.

Type: N/O.

Contact rating: 5A, 240V.

Digital Voltmeter:

Range: 0 to 10Vdc.

Resolution: 10mVdc.

Set Point Generator:

2 Voltages selectable through a switch, which allows generate a step signal.

Amplitude: 0 to 10Vdc.

System Simulator:

Simulates a first order lag System.

Time constant (T): 20s.

Gain 1 to 10 (clockwise direction).

Communication module:

Allows connect to PC using IrDA protocol.

Software: ABB device type manager (DTM), configuration software for Control Master industrial controller versions:

The software allows selection of type of control, industrial controller parameters, setting of alerts and alarms, type of system loop, etc. The access to configuration of different parameters is through a comprehensible Blocks scheme of the system process.

Cables and Accessories, for normal operation.

Manuals:	This unit is supplied with the following manuals: Required Services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices Manuals.

Dimensions:	Main Unit: 490 x 330 x 310 mm. approx. (19.29 x 12.99 x 12.20 inches approx.)   Weight: 10 Kg. approx. (22 pounds approx.)

Communication Module: 100 x 100 x 310 mm. approx. (3.93 x 3.93 x 12.20 inches approx.)   Weight: 1 Kg. approx. (2.2 pounds approx.)

EXERCISES AND PRACTICAL POSSIBILITIES

1.-	Installation, connection and familiarization with the software.

2.-	Study of the transfer function (static and dynamic).

3.-	Familiarize with the Set point generator, generation of a square signal using two analog signals.

4.-	Familiarization with the navigation of an industrial controller (operator page screen, trend display screen, etc).

5.-	Step-response of a first order system.

6.-	Configuration of analog inputs/outputs signals of the industrial controller (electrical range, engineering units, fault detector, etc).

7.-	Manual control of a first order system using an industrial controller (open-loop).

8.-	Automatic PID control of a first order system using an industrial controller (closed loop).

9.-	Obtaining the PID parameters automatically using autotuning.

10.-	Setting alarms and diagnostics generation.

11.-	Setting of an industrial controller using the front panel (configuration level, parameter level, operation control level, etc.).

12.-	Remote setting of an industrial controller using the configuration software (configuration level, parameter level, operation control level, etc.).