# The EDIBON Industrial Controller Networking “CRCI” allows student the familiarization with the function and operation of an industrial process controller network, managed by a central process controller (computer PC).

# The CRCI Unit enables to take the first steps in process automation using field buses, and provide the students the material for analyze a full operative industrial controllers network. It demonstrates the operation of a process control system based on a simple application.

# TENDER SPECIFICATIONS

CRCI is composed of:

Unit (in metallic box), including:

2 Industrial Controllers modules. Each module is composed of:

Industrial Controller:

ABB Controller CM30.

Display: color 1/4 VGA TFT, liquid crystal display (LCD) with built-in backlight.

Language: English, German, French, Italian and Spanish.

Operator keypad: 6 tactile membrane keys.

Password protection: Basic/Advanced user-assigned password protection.

Trend display:

Recording of 2 variables.

Configurable sample rate (1 second to 5 minutes).

Control parameters:

Proportional band: 0 to 999.9 %.

Integral: 0 to 10000 s.

Derivative: 0 to 999.9 s.

Manual Reset 0.0 to 100 %.

Autotune: On-demand calculation of control settings.

Process alarms:

Number: 8.

Types: High/Low process and High / Low latch.

Acknowledgement: Via front panel keys or digital signals.

Source: Fully configurable (for example, PV, analog input, math block inbuilt, OP control loop deviation).

Hysteresis: Level and time.

Alarm enable: Enable/Disable of individual alarms via a digital signal.

Analog inputs:

Number: 2.

Complete configurable process input: voltage (V or mV), current (mA), resistance (ohms), Thermocouple, 3-Wire RTD, frequency, pulse, volt-free digital input and 24V digital input.

Selectable set points via software (remote from the computer) or front panel.

Analog/Digital output:

Number: 1.

Type: configurable as analog or digital pulse.

Analog range: 0 to 20 mA (programmable).

Control output types (Configurable through software):

Current proportioning/Voltage proportioning (using resistor).

Time proportioning.

On/Off.

Motorized valve with feedback.

Motorized valve without feedback.

Split output with combinations of relay digital O/P and current O/Ps.

Relays:

Number: 2. Type: N/O. Contact rating: 5A, 240V.

Communication (PC): RS-485 connector (Profibus DP).

Set Point Generator module:

2 Voltages selectable through a switch, which allows generate a step signal. Amplitude: 0 to 10Vdc.

All process variables are accessible as analog signals at lab jacks.

Possibility of connection of external instruments via lab jacks (for example: line recorder, oscilloscope, etc).

Interface card, with RS-485 connector, to connect the industrial controllers through a field bus (Profibus DP) with the computer (PC).

Software: it includes the OPC server drivers and the Control Configuration Software for the Industrial Controllers.

Cables and Accessories, for normal operation.

Manuals: This unit is supplied with the following manuals: Required Services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices Manuals.

Dimensions: 490 x 330 x 310 mm. approx. (19.29 x 12.99 x 12.20 inches approx.).     Weight: 12 Kg. approx. (26.4 pounds approx.).

EXERCISES AND PRACTICAL POSSIBILITIES

1.-	Installation, connection and familiarization with the software.

2.-	Familiarization with the navigation of an industrial controller (operator page screen, trend display screen, etc).

3.-	Setting up an industrial controller to accommodate the analog inputs/outputs signals types and engineering and electrical units.

4.-	Function of a digital industrial controller.

5.-	Configuration of analog inputs/outputs signals of the industrial controller (electrical range, engineering units, fault detector, etc).

6.-	Setting alarms and diagnostics generation.

To learn and to familiarize with the operation and structure of a process control system under Profibus DP:

7.-	Layout of a field bus system using the Profibus DP field bus.

8.-	Study of OPC (OLE for Process Control) server function.

9.-	Configuration of an industrial controllers networking through the software: Master and slave assignment.

10.-Reading control variables and PID parameters and displaying them on computer (PC) monitor.

11.-Scaling displays.

12.-Setting of an industrial controller using the front panel (configuration level, parameter level, operation control level, etc.).

13.-Remote setting of an industrial controller using the control configuration software (configuration level, parameter level, operation control level, etc.).