# TENDER SPECIFICATIONS

A- STRUCTURAL SPECIFICATIONS:

- Double board of 300 x 210 mm. approx. with separators and with work option in standard base.

- Faults simulation switches.

- Metallic taking of data points (where measures can be taken (voltage, current, resistance, etc.)), and connection cables.

- 25 pines connector for plane cable and for connecting to power supply.

- Serigraphied diagrams of the different circuits.

B- TECHNICAL DATA:

- This module consists of a board for studying Pulse Amplitude Modulation and Demodulation (PAM), and Time Division Multiplex (TDM).

- Sampling and time division multiplex are analyzed for each channel.

- Includes analog tetrapolar switches installed both in the transmitter and the receiver for channel multiplexing and  demultiplexing.

- Input channels: 4 TDM  and  PAM.

- Analog channels: 250 Hz., 500 Hz, 1 KHz, and 2 KHz.

- Sampling frequency: 16 KHz  per channel.

- Sampling utilization factor: variable with transmission from 0 to 90% using 10%  steps per channel.

- Analog channels: 250 Hz., 500 Hz, 1 KHz, and 2 KHz, variable amplitude with potentiometer.

- Low-pass filter cutoff frequency: 3.4 KHz.

- Three operation modes, allowing verification of the receiver's complexity and channel usage, depending on the transmitted information.

- Possibility of transmitting externally supplied signals.

- The board permits introducing faults simulation using a 	switchboard, thus enabling the student to study in depth the board's operation and localization of faults.

- Accessories included, such as cabling, connectors, etc.

- Dimensions: 300 x 210 x 45 mm. approx. Weight: 300 gr. Approx.

- C.A.I. Software System

C- COMPUTER AIDED INSTRUCTION (C.A.I.) SOFTWARE SYSTEM:

This complete System includes INS/SOF (Instructor Software) + (Student/Module Software):

- With the INS/SOF. Classroom Management Software Package (Instructor Software), the Teacher has a whole range of options, among them:

- Organize Students by Classes and Groups.

- Create easily new entries or delete them.

- Create data bases with student information.

- Analyze results and make statistical comparisons.

- Print reports.

- Develop own examinations.

- Detect student’s progress and difficulties.

...and many other facilities.

The Instructor Software is the same for all the modules, and working in network configuration, allows controlling all the students in the classroom.

IMPORTANT: Only one Software package is needed per classroom.

- Computer Aided Instruction Software Package (Student/Module Software):

- It explains how to use the module, run the experiments and what to do at any moment.

- Each module has its own Student Software package.

- The options are presented by pull-down menus an pop-up windows.

- Each Software Package contains:

Theory: that gives the student the theoretical background for a total understanding of the studied subject.

Exercises: divided by thematic areas and chapters to check out that the theory has been understood.

Guided Practices: presents several practices to be done, alongside the modules, showing how to complete the circuits and get the right information from them.

Exams: set of questions presented to test the obtained knowledge.

- LICOMBA/CAL. Software

D- COMPUTER AIDED LEARNING SOFTWARE (RESULTS CALCULATION AND ANALYSIS):

- LICOMBA/CAL. Computer Aided Learning Software (Results Calculation and Analysis):

This computer Aided Learning Software is a Windows based software, simple and very easy to use specifically developed by EDIBON.

CAL is a class assistant that helps in making the necessary calculations to extract the right conclusions from data obtained during the experimental practices.

With a single click, CAL computes the value of all the variables involved. Also, CAL gives the option of plotting and printing the results.

Simply insert the experimental data, with a single click CAL will perform the calculations.

Once the Area of study is selected, the right module can be chosen among a wide range, each one with its own set of lab exercises.

Between the plotting options, any variable can be represented against any other. And there exist a great range of different plotting displays.

Among the given choices, an additional help button can be found, which offers a wide range of information, such as constant values, unit conversion factors and integral and derivative tables.

- EDAS/VIS. EDIBON Data Acquisition System/Virtual Instrumentation System

This EDAS/VIS System includes DAIB + DAB + EDAS/VIS-SOF.

E- HARDWARE FOR DATA ACQUISITION/VIRTUAL INSTRUMENTATION:

- DAIB. Data Acquisition Interface Box:

Steel box. Dimensions: 310x220x145 mm. approx.

Front panel:

16 Analog inputs.

Sampling velocity 1,250,000 samples per second for EDAS/VIS 1.25 Version.

Sampling velocity 250,000 samples per second for EDAS/VIS 0.25 Version.

2 Analog outputs.

24 Digital inputs/outputs, configurable as inputs or outputs, with 24 state led indicators. These digital inputs/outputs are grouped in three ports of eight channels (P0, P1 and P3).

Digital signal simulator. Analog signal simulator. Main ON/OFF switch.

Inside: Internal power supply of 12 and 5 V. Potentiometer.

Back panel: Power supply connector. SCSI connector (for connecting with the data acquisition board).

Connecting cables.

- DAB. Data Acquisition Board:

PCI board (National Instruments) to be placed in a computer slot.

For EDAS/VIS 1.25 Version:

Analog input:

Number of channels = 16 single-ended or 8 differential. Resolution = 16 bits, 1 in 65536.

Sampling rate up to: 1,250,000 S/s (samples per second).

Input range (V) = +/- 10 V. Data transfers =DMA, interrupts, programmed 1/0. Number of DMA channels = 6.

Analog output:

Number of channels = 2. Resolution = 16 bits, 1 in 65536. Maximum output rate up to: 833 KS/s.

Output range (V) = +/- 10 V. Data transfers = DMA, interrupts, programmed 1/0.

Digital Input/Output: Number of channels=24 inputs/outputs. D0 or D1 Sample Clock frequency: 0 to 1 MHz.

Timing: Counter/timers = 2. Resolution: Counter/timers: 32 bits.

For EDAS/VIS 0.25 Version:

This is a similar version to the EDAS/VIS 1.25, with the only difference that for this one, the sampling rate up to 250,000 S/s (samples per second).

F- DATA ACQUISITION/VIRTUAL INSTRUMENTATION SOFTWARE:

- EDAS/VIS-SOF. Data Acquisition and Virtual Instrumentation Software:

Compatible with actual Windows operating systems.

It works as:

- Digital oscilloscope.

- Multimeter.

- Function generator.

- Spectrum analyzer.

- Transient recorder.

- Logic analyzer.

Logic generator.

This amicable graphical interface allows the representation of inputs/outputs temporal evolution.

Configurable software allowing the representation of temporal evolution of the different inputs and outputs.

It stores acquired data in a file (16 analog inputs, 2 analog outputs, 24 digital inputs/outputs at the same time) for further analysis.

Print screens and reports of the signals at any time. Quick capture in a period of time and posterior representation (Sampling and Hold).

Two signal generators, independent for sinusoidal, triangular, saw and square.

Visualization of a tension of the circuits on the computer screen.

Sampling velocity 1,250,000 samples per second for EDAS/VIS 1.25 Version.

Sampling velocity 250,000 samples per second for EDAS/VIS 0.25 Version.

Measurement, analysis, visualization, representation and report of results.

All 16 input channels could be scaled to compare signal with different voltage levels.

IMPORTANT:

Only one EDAS/VIS is needed for all basic electronic boards. One EDAS/VIS is needed for each student work post.

The EDAS/VIS allows to work with several basic electronic boards simultaneously.

G- MANUALS:

This module will be supplied with the following manuals:

- Required services manual.

- Assembly and installation manual.

- Interface and control software manual (if it is necessary).

- Starting-up manual.

- Safety manual.

- Maintenance manual.

- Calibration manual (if it is necessary).

- Practices manual.

H- PRACTICES POSSIBILITIES:

This module is designed to be able to do the following practices:

1.-	Analysis of the principles of Time Division Multiplex (TDM).

2.- 	Analysis of the features of the Transmitter, the Receiver and all the other circuits.

3.-	Comparison between different operation modes, varying with their connections.

4.- 	Faults simulation.