# TENDER SPECIFICATIONS

Motor-Generator Group mounted in a painted steel structure.

Three phase generator of 24 Vac and 11A currents.

This Motor-Generator Group allows the study of the three phase alternator in both no-load and load regime.

Base structure (painted steel).

Couplings.

Connectors.

EMT6/E. Permanent magnets synchronous three-phase generator (24 Vac):

Power: 450 W. Speed: 750 r.p.m. Frequency: 50 Hz. V. armature.: 3 x 24 Vac. I. Armature.: 11A.

EMT7/E. Asynchronous three-phase motor of squirrel cage:

Power: 550 W. Speed: 750 r.p.m. Connections: Triangle/Star. Frequency: 50-60 Hz. V. Armature: 3 x 230/400 V. I. Armature nominal:3,6-2A.

Protections cover.

Cables and accessories, for normal operation.

Manuals: This unit is supplied with the following manuals: Required Services, Assembly and  Installation, Starting-up, Safety, Maintenance & Practices Manuals.

Dimensions: 750 x 250 x 250 mm. approx.  Weight: 35 Kg. approx.

EXERCISES AND PRACTICAL POSSIBILITIES

Some Practical Possibilities of the Unit:

1.- Measurements of voltage with no load, measurement of the frequency and measurement of no load losses.

2.- Connection to a load. Measurement of the voltage drop with load. Measurement of the power supplied.

3.- Behaviour of the alternator with different cos  loads.