The Electrical Machines Unit (EME/B), is a compact and robust box for the study of the main electrical functions. In its front side, you find standard electrical functions, divided in sections, for a better visualization of the different applications.

TENDER SPECIFICATIONS

Metallic box.

Diagram in the front panel.

Thermal Magnetic Circuit Breaker.

DC supply 200 Vdc with fuses.

Connection Key

Emergency stop push button.

Two push buttons (1 NO + 1 NC).

One contactor, with three power connections, one control connection and supply control.

*Minimum recommended measurement units:

2 Digital Multimeters.

Recommended measurement unit:

EAL. Network Analyzer Unit.

Electrical supply required: Three-phase with neutral and ground, 380 V.

Dimensions: 300 x 190 x 120 mm. approx. Weight: 5 Kg. approx.

EXERCISES AND PRACTICAL POSSIBILITIES

Some Practical Possibilities of the Unit:

The D.C.Machine:

1.-	Preparation, regulation in a dynamo with independent excitation.

2.-	Dynamos with series and shunt excitation.

3.-	Speed control at constant torque.

4.-	Series D.C. Motor: starting, speed variation, inversion and braking.

The Asynchronous Machine:

5.-	Starting process of a three-phase asynchronous motor with rotor in short circuit.

6.-	Test without load of an asynchronous motor with rotor in short circuit.

The Universal motor:

7.-	The Universal motor with D.C. supply.